## Slide 1: ITERATIVE METHODS
Numerical methods in chemical engineering
Ivo Roghair

## Slide 2: OVERVIEW
Sparse matrices
Large systems of linear equations
Iterative methods for large systems of equations
  Jacobi method
  Gauss-Seidel method
Notes: Today we are going to take a look at iterative methods that can be used to solve large systems of (linear) equations.
We will solve Laplace’s equation, that describes heat conduction in a rectangular geometry.

## Slide 3: Sparse matrices
In many engineering cases, we deal with sparse matrices (as opposed to dense matrices)
  A matrix is sparse when it mostly consists of zeros
  Linear systems where equations depend on a limited number of variables (e.g. spatial discretization)
Storing zeros is not very efficient:
    >> A = eye(10000);
    >> whos A
    >> S = sparse(A);
    >> whos S
Can you think of a way to achieve this?
Sparse matrix formats: Yale, CRS, CCS

## Slide 4: Sparse matrices
Example: Yale storage format, storing 3 vectors:
  A = [ 5 8 3 6 ]
  IA = [ 0 0 2 3 4 ]
  JA = [ 0 1 2 1 ]
A stores the nonzero values
IA(i) stores the index in A of the first non-zero in row i
JA stores the column index
Zero-based indices

## Slide 5: Sparse matrices

## Slide 6: LAPLACE’S EQUATIONS
T
t
T
2
Ñ
=
¶
¶
a
Thermal diffusivity
The steady state problem:
0
0
2
2
2
2
2
=
¶
¶
+
¶
¶
=
Ñ
y
T
x
T
T
x
y
T=Tb1
T=Tb2
T=Tb4
T=Tb3
Notes: The equation that governs temperature in a slab of material is given by (4-1). Where a is the thermal diffusivity. Nabla, or del is the partial derivative operator. We will consider this equation as a steady state problem, so no dependence of time (as 4-2). If we write out (4-2) in two dimensions, for Cartesian coordinates we will have (4-3).
The figure shows you how the domain is defined, with four boundaries.

## Slide 7: TRACK TEMPERATURE ON A GRID
i =1
i =2
i =3
j =1
j =2
j =3
T1
T2
T3
TNx+1
TNx+2
TNx+3
i =Nx
j =Ny
…
…
TNx
T2Nx
(Ny-1)Nx+1
Index of a node is given by:
k = i + Nx(j-1)
So that:
Ti,j = Tk=i+Nx(j-1)
Notes: We now place a grid over the domain and we want to track the temperature at each point on the grid. For simplicity we will use an equally divided grid interval, so Dx = Dy.
We can index a node with
K = i + Nx(j-1)
So that: Ti,j = Tk=i+Nx(j-1)
Now we can use finite differences to approximate a our two dimensional Laplace equation. So we need some kind of estimate of the second derivative at node k.

## Slide 8: ESTIMATES OF THE SECOND DIFFERENTIALS FOR x
Assume a piece-wise linear profile in the temperature, e.g.:
Ti+1
Ti
Ti-1
Dx
Dx
x
T
x
x
T
x
T
x
T
i
i
D
¶
¶
-
¶
¶
»
¶
¶
-
+
2
/
1
2
/
1
2
2
(
)
(
)
2
,
1
,
,
1
,
1
,
,
,
1
2
x
T
T
T
x
x
T
T
x
T
T
j
i
j
i
j
i
j
i
j
i
j
i
j
i
D
+
-
=
D
D
-
-
D
-
»
-
+
-
+
Notes: We could assume a piece-wise linear profile, where we approximate at each grid interval a temperature difference by a linear function. We can estimate now the second derivative by (4-4), which can be written as (4-5)

## Slide 9: INCLUDE THE ESTIMATES OF THE SECOND DIFFERENTIALS FOR y
0
2
2
2
,
1
,
,
1
2
,
1
,
,
1
=
D
+
-
+
D
+
-
-
+
-
+
y
T
T
T
x
T
T
T
j
i
j
i
j
i
j
i
j
i
j
i
Equal spaced grid Dx = Dy =1
0
4
1
1
=
+
+
-
+
+
+
-
-
Nx
k
k
k
k
Nx
k
T
T
T
T
T
0
2
2
2
2
1
1
=
D
-
-
+
D
-
-
-
+
-
+
y
T
T
T
x
T
T
T
Nx
k
k
Nx
k
k
k
k
b
AT
=
Notes: Doing the same for the y-direction, we end up with (4-6). Or, in terms of node indices as (4-7). If we take an equally spaced grid of Dx=Dy=1, we can rewrite (4-7) into (4-8). This equations tells you that the temperature at a grid point is equal to the average of the surrounding temperatures.

## Slide 10: LET’S WRITE THIS STUFF AS MATRIX EQUATIONS
Nx=5; %number of points along x direction
Ny=5; %number of points in the y direction
e = ones(Nx*Ny,1);
A = spdiags([e,e,-4*e,e,e],[-Nx,-1,0,1,Nx],Nx*Ny,Nx*Ny);
Notes: If you want to create this system in MATLAB you could type the code above.

## Slide 11: MATRIX SPARSITY
spy(A) Nx=Ny = 5
A sparse matrix structure,
which is not tridiagonal: there are offset bands.
Offset bands can cause your trouble!!
0
5
10
15
20
25
0
5
10
15
20
25
nz = 113
Notes: If you ‘spy’ the A matrix you will see that the matrix has a sparse structure, all elements with values appear in diagonals, the upper and lower parts of the matrix are zeros. It is also not triagonal, as there are offset bands. Such offset bands can cause you a lot of problems!!

## Slide 12: LU decomposition
0
10
20
0
5
10
15
20
25
nz = 129
0
10
20
0
5
10
15
20
25
nz = 129
[L,U,P] = lu(A)
subplot(1,2,1)
spy(L)
subplot(1,2,2)
spy(U)
With LU decomposition we produce matrices that are less sparse than the original matrix.
Sparse storage often required, and also numerical techniques that fully utilizes this!
Notes: What will happen if we do Gaussian elimination, by LU factorization? You could use the command lu. When we factorize matrix A into L,U and P, we produce matrices that are less sparse than the original matrix. We have filled the elements between the offset- and central band diagonals.

## Slide 13: How to impose boundary conditions?
For the nodes on the boundary, we have a simple equation:
However, we have set all nodes to be a function of their neighbors…
  Find the boundary node indices using k = i + Nx(j-1)
    i = 1, j = 1:Ny
    i = Nx, j = 1:Ny
    j = 1, i = 1:Nx
    j = Ny, i = 1:Nx
  Reset the row in A to zeros, set Akk = 1
  Set value in rhs: bk = Tboundary
Boundary conditions are often more elaborate to implement!
Notes: For the nodes on the boundaries, we have a simple equation (4-9). With our previous equation and with our boundaries we end up with a matrix equation, (4-10), a linear system. If you take Nx=Ny=5, your A matrix will be a 25x25 matrix and your T and b will be vectors with 25 elements

## Slide 14: A full program, including solver, may look like (OASE):
function [x,y,T,A] = solveLaplaceEq(Nx,Ny)
% Solves the Laplace equation for steady-state heat conduction
if (nargin < 2)
Nx = 5;
Ny = 5;
end
d = 1/Nx; % Grid spacing
alpha = 1; % Heat conduction
Tb = [10 20 30 40]; % Fixed boundary temperatures
% Fill sparse matrix with [1 1 -4 1 1]
e = ones(Nx*Ny,1);
A = spdiags([e,e,-4*e,e,e],[-Nx,-1,0,1,Nx],Nx*Ny,Nx*Ny);
A = A*alpha/d^2; % This doesnt matter, steady state...
b = zeros(Nx*Ny,1); % Right hand side vector
[A,b] = setBoundaryConditions(A,b,Tb,Nx,Ny);% Set boundary conditions
T = A\b; % Solve matrix
Tc = reshape(T,[Nx,Ny]); % Reshape x-vec to mat Nx,Ny
[xc yc] = meshgrid(1:Nx,1:Ny); % Get position arrays
surf(xc,yc,Tc) % Surface plot
Notes: If you want to create this system in MATLAB you could type the code above.

## Slide 15: Solution to the Laplace equation
Solve the system with \, here for 20x20 and boundaries:
Tb1 = 10
Tb2 = 20
Tb3 = 30
Tb4 = 40
Notes: You could solve now the linear system with T = A\b, for the boundaries Tb1 = 10 and Tb2=Tb3=Tb4 = 0, you could obtain a profile as given in the figura above

## Slide 16: LU DECOMPOSITION
Gaussian elimination on a matrix like A requires more memory (with 3D problems, the offset in the diagonal would even be bigger!)
In general extra memory allocation will not be a problem for MATLAB
MATLAB is clever, in that sense that it attempts to reorder equations, to move elements closer to the diagonal)
Notes: Doing Gaussian elimination on a matrix like A, requires storage of more elements as the algorithm proceeds. If we had taken a 3D problem, we would have had another offset diagonal band, even further from the central band.
The matrix produced by elimination takes up a lot of memory. But, for MATLAB this is not a problem (it allocates extra memory). MATLAB also reorders the equations, so that elements are moved closer to the diagonal.

## Slide 17: Iterative methods
Alternatives for Gaussian elimination
Use iterative methods when systems are large and sparse.
Often such systems are encountered when we want to solve PDE’s of higher dimensions (>1D)
Notes: Concluding, Gaussian elimination is not ideal for solving sparse systems. If we are dealing with large sparse systems of equations we can take resort to iterative methods.
In the early days of computing, iterative methods were important, because memory was limited.

## Slide 18: Examples of iterative methods
Jacobi method
Gauss-Seidel method
Succesive over relaxation
bicg – Bi-conjugate gradient method
pcg – preconditioned conjugate gradient method
gmres – generalized minimum residuals method
bicgstab – Bi-conjugate gradient method
Notes: There are several iterative methods at our hands, for example, the Jacobi method, the Gauss-Sidel method and succesive over relaxation. MATLAB has some functions for iterative methods, it wouldn't hurt you to take a look at them (e.g. by typing help bicg or going to the mathworks website). In this lecture we will look at one method, the Jacobi method.

## Slide 19: The Jacobi method
In our example we derived the following equation:
Rearranging gives:
0
4
1
1
=
+
+
-
+
+
+
-
-
Nx
k
k
k
k
Nx
k
T
T
T
T
T
4
1
1
Nx
k
k
k
Nx
k
k
T
T
T
T
T
+
+
-
-
+
+
+
=
Notes: As you remember we derived an equation in the previous slides (4-11). We could rearrange that equation into (4-12).

## Slide 20: THE JACOBI METHOD
In the Jacobi scheme the iteration proceeds as follows:
  Start with an initial guess for the values of T at each node, we calculate an new, updated values using the equation of the previous slide and store a new vector:
  Do this for all other nodes, and use new values as guess, Repeat!
4
,
,
1
,
1
,
,
old
Nx
k
old
k
old
k
old
Nx
k
new
k
T
T
T
T
T
+
+
-
-
+
+
+
=
Notes: In the Jacobi scheme, the iteration continues with an initial guess for the values of T at each node, we make a new updated value using (4-12) and obtaining (4-13). We do this for all other nodes. Once we have gone through all nodes, we use the new guess values as a guess and repeat!

## Slide 21: NOW WITH MATRICES
÷
÷
÷
÷
÷
÷
÷
÷
ø
ö
ç
ç
ç
ç
ç
ç
ç
ç
è
æ
=
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
A
÷
÷
÷
÷
÷
÷
÷
÷
ø
ö
ç
ç
ç
ç
ç
ç
ç
ç
è
æ
+
÷
÷
÷
÷
÷
÷
÷
÷
ø
ö
ç
ç
ç
ç
ç
ç
ç
ç
è
æ
=
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
A
Consider a matrix A:
Split it into a diagonal matrix D and another matrix S:
Notes: We could use the approach, using matrices,where we start we a matrix a generally of the form in the left upper corner. We split this matrix into a diagonal matrix D and another matrix S.

## Slide 22: SOLVE AT-b
Now we can solve AT=b by:
  (D+S).T = b
  D.T = b –S.T
  D.Tnew = b – S.Told
  Tnew = D-1(b-S.Told)
See Wikipedia: Jacobi_method
Notes: We now can solve AT=b, by the following steps.

## Slide 23: DIAGRAM OF JACOBI METHOD
Only two vectors need to be stored: the old x (k) and the new x (k+1)
Set Told = a gues
Calculate the new node temperature from the guessed (previous) values
Is max(Tnew-Told) < tolerance?
Report the answer as Tnew
Set Told = Tnew
Have all nodes been updated?
YES
YES
NO
NO
Move to next node
Exercise: implement this method and solve a (small) Ax=b system
Notes: The scheme would look like this, the major advantage is that only two vectors need to be stored, the old- and new temperature.

## Slide 24: The core of the solver may look like:
Resetting the sum for each row
Convergence criterion
Store the previous solution
Protection against infinite loops
while ( norm(A*x-b, 2) > err && it_jac < 1000 )
x_old = x;
for i=1:N
s = 0;
for j = 1:N
if (j ~= i)
% Sum off-diagonal*x_old
s = s+A(i,j)*x_old(j);
end
end
% Compute new x value
x(i) = (b(i)-s)/A(i,i);
end
% Increate number of iterations
it_jac = it_jac+1;
end
Nested loops, conditional statement, scalar computations. This makes Matlab slow. It is much better at performing matrix operations as a whole!
Notes: If you want to create this system in MATLAB you could type the code above.

## Slide 25: A few remarks on the implementation
Convergence criterion considerations
  Compare current and previous solution
  Compare Ax and b
  Based on the norm of a vector. Which one?
    L1-norm (sum)
    L2-norm (Euclidian distance)
    L∞-norm (max)
Number of iterations
  May be used to detect non-converging cases.
Start vector x
  Not shown in the previous example, but should be there
  Can have huge impact on performance!

## Slide 26: The solver using array indices:
function [x0,it_jac] = solveJacobi(A,b,tol)
% Set default error
if nargin < 3
tol = 1e-6;
end
x0 = 25*ones(size(b)); % Initial guess
x = zeros(size(b)); % Pre-allocate vector x
N = length(A); % Number of equations
it_jac = 1; % Init number of iterations
% --- Initial iteration to get x here ---
while ( norm(x-x0, 1) > tol > tol && it_jac < 1000 )
x0 = x;
for i = 1:N
x(i) = (1/A(i,i))*((b(i) - A(i,[1:i-1,i+1:N]) * ...
x0([1:i-1,i+1:N])));
end
it_jac = it_jac + 1;
end
it_jac
Notes: If you want to create this system in MATLAB you could type the code above.

## Slide 27: Iterations…
it=1
it=3
it=2
it=10

## Slide 28: Gauss-Seidel method
Gauss-Seidel method is quite similar to Jacobi method
Define a lower and strictly upper triangular matrix, such that A = L + U
  (L+U)x=b
  Lx = b-Ux
  Lxnew = b – Uxold
  xnew = L-1(b-Uxold)
See Wikipedia: Gauss-Seidel_method

## Slide 29: CONVERGENCE OF THE METHOD
Now we define an error at the k-th iteration:
  errork =Tk - T
The error at the next iteration is:
  Tk+1 = D-1(b-S.Tk)
  Errork+1 +T = D-1(b-S.errork-S.T)
  D.errork+1=-S.errork
  Errork+1 = -D-1S.errork
Eigenvalues of D-1S must always have modulus < 1, to ensure that |errork+1| < |errork|
Notes: If we define an error at the k-th iteration, and substituting this into the previous equation, we obtain a formulation of the error at the next iteration. The eigenvalues of D-1S must always have a modulus less than unity to ensure that the error of the new iteration is smaller than the previous one (otherwise the error propagates!)

## Slide 30: CONVERGENGE OF THE METHOD
We can express the vector of error in terms of eigenvectors of D-1S:
  error= a1u1 + a2u2 + a3u3 + a4u4 +…
So:
  errork+1 = -D-1S(a1u1 + a2u2 + a3u3 + a4u4 +…)
        = -a1D-1Su1-a2D-1Su2-a3D-1Su3-a4D-1Su4 +…
        = -a1l1u1-a2l2u2-a3l3u3-a4l4u4 +…
The magnitude of the error will grow each iteration, if l‘s have a complex module >1, So: Find the largest magnitude of eigenvalues for the matrix D-1S
(4-14)
(4-15)
Notes: We could express the error vector in terms of eigenvectors of D-1S as (4-14), so the error at the k+1-th position would be like (4-15).
The magnitude of the error will grow on each iteration if any of the eigenvalues (l) have a complex modulus greater than unity! We should find the largest magnitude of eigenvalue for the matrix D-1S.

## Slide 31: GERSHGORIN’S THEOREM
For a square matrix and row k, an eigenvalue is located on the complex plane within a radius equal or less to the sum of the moduli of the off-diagonal elements of that row.
|
|
|
|
|
|
...
|
|
|
|
|
|
,
1
,
2
,
2
,
1
,
,
N
k
N
k
N
k
k
k
k
k
m
m
m
m
m
m
+
+
+
+
+
£
-
-
-
l
Re(l)
Im(l)
mk,k
Radius = sum of moduli of off-diagonal elements
The eigenvalue lk must be in this circle.
(4-16)
Notes: The eigenvalues must be within this circle for the method to be converging.
Now, Gershgorin’s theorem is introduced.

## Slide 32: APPLICATION OF GERSHGORIN’S THEOREM
Appying Gershgorin’s theorem to our Jacobi iteration, the off-diagonal elements of row k of D-1S are 1/ak.k times the off-diagonal elements of our original matrix A, while the diagonal element is zero:
For |lk|<1:
å
¹
<
k
j
k
k
j
k
a
a
|
|
|
|
,
,
Stability: size of diagonal element must be larger that the sum of moduli of the other elements, such matrix is called diagonally dominant.
(4-17)
Notes: That means, for the Jacobi iteration that the off-diagonal elements of row k of D-1S are 1/ak,k times the off diagonal elements of the original matrix A, while the diagonal element is zero, implying:
|lk||ak,k| = |ak,1| + |ak,2| + …+ |ak,N-2| + |ak,N-1| +|ak,N|
So for|lk|<1 holds (4-17). In words that means, for the Jacobi method to be stable, the size of the diagonal element must be larger than the sum of the moduli of the other elements in the row. Such matrix is called diagonally dominant. It turns out that for the sorts of banded matrices you find when solving pde’s, the this condition is required for stability.

## Slide 33: SUMMARY
Partial differential equations can be written as sparse systems of linear equations
Sparse systems can be handled with a direct method like Gaussian elimination
If you have systems of more than 1 dimension, a direct method still can be used, if there are no memory issues, otherwise an iterative method may be attractive.
The Jacobi method was introduced. Many other methods are based on the Jacobi method (SOR method, for example)
Notes: The main message of this lecture was: pde’s can be written as sparse systems of linear equations. You could use a direct method, like Gaussian elimination to solve such system, but, if you have systems in more then 1 dimension, there are more efficient alternatives: iterative methods. You saw, briefly how the Jacobi method works, and you found out that eigenvalues of composite matrices, representing error in the iteration determine whether the method is stable or not (that means the error converges).